## Slide 1
Programmable Characterisation of
3D-Printed Wind Turbine Blades
Stephen S. Eacuello, ISE Ph.D. Candidate
Department of Mechanical, Industrial and Systems Engineering
Introduction
3D printing makes rotor geometry cheap to iterate. Measuring whether a change actually helped does not follow automatically.
A campaign comparing a dozen blades has to hold its protocol fixed across weeks, or the comparison silently becomes a comparison of settings.
This work builds programmable, reproducible control of the Aerolab tunnel and its electronic load, so a rotor is characterised unattended in ~10 minutes with a machine-checkable record of exactly how.
▪ Automated 14-point load sweep, drive and load on one clock
▪ Two-layer watchdog safety, hardware E-stop untouched
▪ Protocol fingerprinting so runs are provably comparable
▪ Live dashboard, digital twin, and a full parameter archive
System Architecture
Drive ABB ACS550-U1-046A-2, 15 HP, 208–240 V 3φ. Commands speed in rpm, full scale 2435
Controller Portenta Machine Control — sole Modbus RTU master, owns both watchdogs
Load Chroma 63004-150-60 DC electronic load, SCPI over USB-TMC
Wind 10.1 – 37.5 m/s; v = 0.02132·rpm − 0.424, R² = 0.9996
The hardwired E-stop is the safety device. No software is in that chain.
• Two independent watchdogs — the drive stops the fan if the PMC goes quiet (3.0 s); the PMC stops the fan if the host goes quiet (5.0 s). Neither depends on the layer above it.
• One Modbus master only. Two devices commanding a 15 HP fan, neither aware of the other, is the failure this design prevents.
• Interlock: load ON → wind UP → test → wind DOWN → load OFF. An unloaded rotor in moving air accelerates.
FIGURE
docs/diagrams/system_overview.png
Measurement and control chain
Project Details
At each of 14 wind speeds (500 → 1800 rpm fan, 100 rpm steps):
• Ramp the electronic load in constant-current steps
• Stop once electrical power falls to 80% of its peak — the rotor is never driven to stall
• Record V and I at every step, unload, advance the wind
Peak located by parabolic fit. Over a flat maximum the largest single sample is biased high, and the bias grows with sample count — so blades measured with different point counts would be compared unfairly.
Protocol fingerprinting. Every run hashes the settings that change what a curve means. Runs with different fingerprints are not comparable, and the hash makes that visible instead of silent.
Rotor vertical-axis H-rotor, 3 blades, R = 101.6 mm, span 245 mm. Swept area 2RH = 0.0498 m² — a cylinder, not a disc.
Blade PETG thin cambered plate: 1.79 mm wall, t/c 4%, 42% camber, 183° turning, square edges — not an airfoil.
FIGURE
docs/diagrams/sweep_protocol.png
Outer loop = wind speed; inner loop = load current
Results
14 / 14 points clean, single continuous run
P ∝ v^3.77 R² = 0.998
peak 3.793 W at 37.5 m/s
Independent repeats at 1200 and 1800 rpm match the sweep to 0.3% and 0.2%.
THE EXPONENT IS A GENERATOR CHARACTERISTIC, NOT AN AERODYNAMIC ONE
V_oc ∝ v^1.52 and R_int ∝ v^−0.64 (73.6 → 40.1 Ω)
every peak sits at the Thévenin match, P = V_oc² / 4R_int
n = 2a − b = 3.69, against 3.77 measured
Cp_elec = 0.10 – 0.24%, ~100× below a working H-rotor: peak power sits at ω/ω_runaway ≈ 0.70 → 0.94, the far limb of Cp(λ) where Cp → 0 by construction.
fan rpm | m/s | P_max | at
496 | 10.1 | 0.030 W | 0.018 A
894 | 18.6 | 0.273 W | 0.068 A
1384 | 29.1 | 1.665 W | 0.240 A
1779 | 37.5 | 3.793 W | 0.320 A
Wind speed from MEASURED fan rpm — the drive settles 4–13 rpm below setpoint.
Conclusion
A better blade can read as LESS electrical power. Anything raising Cp_max while adding low-α drag lowers λ_runaway, lowers V_oc, and lowers measured P as the square.
One rotor-speed channel converts the entire existing archive into Cq(λ) retroactively — every sweep already records a full load ramp at all 14 wind speeds, and a proximity sensor on the rig already feeds the DAQ. What is needed is its channel and pulses-per-revolution, not new hardware.
Limits: electrical power only, not Cp · Re_chord 32,376–119,735, below Reynolds-independence (~2×10⁵) · generator R_int inferred, never measured · single-mount data, no mount-to-mount error bar yet.
The University of Rhode Island CYPHER Research Center IPT Meeting for Power Systems and Manufacturing
This research was supported by the Office of Naval Research under Grant No. N00014-24-1-2129.
The views and conclusions contained in this poster are those of the authors and should not be interpreted as representing the official policies, either expressed or implied, of the Office of Naval Research or the U.S. Government