## Slide 1
UNIVERSITY OF RHODE ISLAND · SODHI LAB × JEONG LAB
Programmable Characterisation of
3D-Printed Wind Turbine Blades
Automated load sweeps in the Aerolab wind tunnel
Stephen Acuello
seacuello@uri.edu · 26 August 2026
Notes: Setup pair = slides 2-3. Results pair = slides 4-5. Slides 6-7 are optional; 6 is the ask.

## Slide 2
SLIDE 1 OF 2 · EXPERIMENTAL SETUP
The Rig
FIGURE
docs/diagrams/system_overview.png
Full measurement and control chain
CONTROL CHAIN
Drive — ABB ACS550-U1-046A-2, 15 HP, 208–240 V 3φ. Commands speed in rpm; full scale 2435
Path — Python host → USB → Portenta Machine Control → RS-485 Modbus RTU → drive
Load — Chroma 63004-150-60. Sets the rotor's operating point and is the best V/I instrument on the rig
Wind — 500–1800 rpm fan = 10.1–37.5 m/s, v = 0.02132·rpm − 0.424 (R² = 0.9996)
Bandwidth — τ = 0.63 ± 0.12 s, from five 1-cosine gusts
ROTOR UNDER TEST
Vertical-axis H-rotor, 3 blades, R = 101.6 mm, span 245 mm. Swept area 2RH = 0.0498 m² — a cylinder, not a disc.
Blade section: thin cambered plate, 1.79 mm wall, t/c 4%, 42% camber, 183° turning, square edges.
Notes: Swept area is 2RH because it is a VAWT. Using pi*R^2 overstates Cp by 1.54x. The blade is a cambered plate, NOT an airfoil - it matters for any polar or XFOIL cross-check.

## Slide 3
SLIDE 2 OF 2 · EXPERIMENTAL SETUP
Safety Architecture
The hardwired E-stop is the safety device.
No software is in that chain. Everything below reduces how often it is needed — none of it replaces it.
TWO INDEPENDENT WATCHDOGS
• The drive stops the fan if the PMC goes quiet — par 3018/3019, 3.0 s
• The PMC stops the fan if the host goes quiet — 5.0 s
• Neither depends on the layer above it being correct
ONE MODBUS MASTER ONLY
• The PMC is the master. Modbus RTU permits exactly one
• A direct host-to-drive cable must never be landed at the same time
• Two devices commanding a 15 HP fan, neither aware of the other, is the failure this design exists to prevent
TURBINE INTERLOCK
load ON → wind UP → test → wind DOWN → load OFF
• An unloaded rotor in moving air accelerates until something mechanical stops it
• If the fan cannot be confirmed stopped, the load stays on
Notes: The two watchdogs are the slide's point: each layer is watched by the layer BELOW it, so the host being wrong cannot run the fan away.

## Slide 4
SLIDE 1 OF 2 · RESULTS
Method
Automated blade characterisation — ~10 minutes per rotor, unattended, 14 wind speeds
FIGURE
docs/diagrams/sweep_protocol.png
Outer loop = wind speed; inner loop = load current
AT EACH WIND SPEED
• Ramp the electronic load in constant-current steps
• Stop once electrical power falls to 80% of its peak — the rotor is never driven to stall
• Record V and I at every step, unload, advance the wind
WHY A PARABOLIC FIT
The top of P(I) is flat. The largest single sample is biased high, and the bias grows with the number of samples — so two blades measured with different point counts would be compared unfairly.
PROTOCOL FINGERPRINT
Every run carries one. Runs measured under different settings are not comparable — the fingerprint makes that visible instead of silent.
Notes: The fingerprint is the campaign's integrity mechanism. Across a dozen rotors it is very easy to change a setting by accident and impossible to spot afterwards - the numbers stay plausible.

## Slide 5
SLIDE 2 OF 2 · RESULTS
Blade v1, Ra 20 µm
fan rpm cmd | measured | m/s | P_max | at
500 | 496 | 10.1 | 0.030 W | 0.018 A
900 | 894 | 18.6 | 0.273 W | 0.068 A
1400 | 1384 | 29.1 | 1.665 W | 0.240 A
1800 | 1779 | 37.5 | 3.793 W | 0.320 A
Wind speed is derived from MEASURED fan rpm, not commanded — the drive settles 4–13 rpm below setpoint.
WHAT IS SOLID
• 14 / 14 points clean, single continuous run
• P ∝ v^3.77, R² = 0.998 across 10.1–37.5 m/s
• Independent repeats at 1200 and 1800 rpm match to 0.3% / 0.2%
WHAT IT DOES NOT YET SHOW
This is electrical power at the load terminals — not Cp.
The v^3.77 exponent decomposes almost entirely into the generator, not the rotor:
  V_oc ∝ v^1.52 and R_int ∝ v^−0.64 (73.6 → 40.1 Ω)
  every peak sits at the Thévenin match, P = V_oc²/4R_int
  n = 2a − b = 3.69, against 3.77 measured
→ Little aerodynamic residual is left for the blade to move. Without rotor speed, blade comparisons partly compare the generator.
Cp_elec = 0.10–0.24%, roughly 100× below a working H-rotor, because peak power sits at ω/ω_runaway ≈ 0.70→0.94 — the far limb of Cp(λ) where Cp → 0 by construction.
Notes: Do NOT present v^3.77 as 'Cp still climbing with Reynolds'. A 9-agent audit on 25 Aug showed the exponent is a generator characteristic: V_oc ~ v^1.52, R_int ~ v^-0.64, n = 2a-b = 3.69. The honest version is stronger and it is the argument for slide 6.

## Slide 6
OPTIONAL · THE NEXT MEASUREMENT
One Channel Unlocks Cp(λ)
The rotor-speed measurement already exists in the Jeong lab DAQ.
A proximity sensor on the rig already records it. What is needed is its channel number and pulses-per-revolution — not new hardware.
WHY IT MATTERS MORE THAN ANY BLADE RUN
• Without ω there is no λ and no Cp, so the rig cannot separate rotor aerodynamics from generator matching.
• A better blade can read as LESS power: anything that raises Cp_max while adding low-α drag lowers λ_runaway, lowers V_oc, and lowers measured P as the SQUARE of the speed change.
• Two rotors with Cp_max of 5% and 25% would rank purely by how freely they spin.
THE PAYOFF IS RETROACTIVE
Every sweep_*_points.csv already holds a full load ramp at all 14 wind speeds. Adding one rotor-speed channel converts the entire existing archive into a Cq(λ) traverse — without another minute of tunnel time.
ALSO USEFUL, AND ALREADY BUILT
Fan rpm now leaves the PMC as a 0–10 V analog signal for the DAQ (0.5 V + rpm/300), so fan speed and rotor speed share one time base. 0.000 V is a live zero meaning INVALID, not zero rpm.
Notes: This is the ask, aimed at the person who owns the DAQ. Keep it concrete: channel number and pulses-per-rev, that is all.

## Slide 7
OPTIONAL · STATED PLAINLY
Known Limitations
Every one of these was found by adversarial review of our own results, and each is recorded in the repository.
Not Cp
Electrical power only. Cp(λ) needs the rotor-speed channel; every blade tested before that lands must be re-run to obtain λ.
The blade is not an airfoil
1.79 mm constant wall, t/c 4%, 42% camber, 183° turning, square-cut edges. Separation is pinned by geometry, so any XFOIL or polar cross-check is answering a question about a different part.
Reynolds range
Re_chord = 32,376 → 119,735. Below Reynolds-independence for a cross-flow turbine (~2×10⁵), so absolute performance is not transferable to full scale.
Generator not characterised
R_int is inferred from a curve fit and has never been measured directly. It gates every derived quantity.
Wind speed disagreement
Summary and points files differ by 1.1–1.2% at the same fan set point. At v^3.77 that is 4.5% in power. Unresolved — flagged, not averaged away.
Single-mount data
Every result so far comes from one mounting of one rotor. There is no mount-to-mount error bar yet; the ABBA protocol for the next session produces the first one.
Notes: Optional slide. For an academic audience this is the most credible thing in the deck - it shows the limits are known and quantified rather than unexamined.