## Slide 1
EXPERIMENTAL RECORD
Surface Roughness Study of a Vertical-Axis Wind Turbine
Experimental setup, three recovered test records, and requirements for a defensible roughness comparison
Stephen Eacuello · Taegu Kang
September 2026

## Slide 2
EXPERIMENTAL SETUP · 1 OF 2
Automated control synchronizes wind, load, and electrical capture
Aerolab tunnel · 14 wind setpoints · 10.1–37.5 m/s · point-level and summary records
Python host
Executes each setpoint and writes the run record
Portenta PMC
USB interface and sole Modbus RTU master
ABB ACS550
Commands fan speed and records measured rpm
Wind tunnel + VAWT
Three-blade vertical-axis test rotor
Generator + Chroma
Applies load and measures rectified electrical output
Test article and operating range
Rotor | R = 101.6 mm; span = 245 mm
Swept area | 2RH = 0.0498 m²
Automated sweep | 14 points; 500–1800 fan rpm
Wind range | 10.1–37.5 m/s
Blade sets | Smooth/Ra20/Ra80 recorded; Ra40 missing
Recorded at every load step
• Measured fan rpm and calibrated wind speed • Terminal voltage, current, and electrical power • Drive status and protocol fingerprint • Point-level and summary CSVs
Key limitation: rotor rpm was not recorded on the common DAQ time base.
Source: rig documentation and automated-test repository. · Stephen Eacuello and Taegu Kang

## Slide 3
EXPERIMENTAL SETUP · 2 OF 2
The automated protocol standardizes each point and fails safe
14 wind setpoints · load-current sweep · local quadratic Pmax fit · ~10 min per rotor
01
Set wind
Command fan rpm; begin only after measured speed stabilizes.
02
Sweep load
Sweep load current while logging voltage, current, power, and measured fan rpm.
03
Estimate Pmax
Fit a local quadratic around the highest-power samples; reject isolated noise peaks.
04
Unload and advance
Stop near 80% of fitted peak; unload, save both records, and advance.
Independent safeguards
Hardwired E-stop
Primary protection remains independent of software.
3 s drive watchdog
Drive stops if PMC communication is lost.
5 s host watchdog
PMC unloads and stops if Python communication is lost.
One Modbus master
Prevents competing commands to the drive.
Traceability: each run saves point-level data, summary data, and the full protocol fingerprint.
Interlock: load ON → wind UP → test → wind DOWN → load OFF
Source: control implementation, drive parameters, and automated sweep protocol.

## Slide 4
KEY DATA & RESULTS · 1 OF 5
Ra20 peak electrical power rises monotonically to 3.79 W
Across 10.1–37.5 m/s, duplicate checks agree within 0.3%
Chart: Peak electrical power vs measured wind speed
| 10.1 | 18.6 | 29.1 | 37.5
Pmax (W) | 0.03 | 0.273 | 1.665 | 3.793
14 measured points
Complete automated sweep; four audited points shown
≤0.3% difference
Agreement at both repeated check points
n = 3.77; R² = 0.998
Power-law fit: Pmax ∝ v³·⁷⁷
Fan rpm | Wind (m/s) | Pmax (W) | I at Pmax (A)
496 | 10.1 | 0.030 | 0.018
894 | 18.6 | 0.273 | 0.068
1384 | 29.1 | 1.665 | 0.240
1779 | 37.5 | 3.793 | 0.320
Measured fan rpm sets wind speed. Rotor rpm was not synchronized, so aerodynamic coefficients cannot yet be compared.
Source: sweep_v1_Ra20 summary and repeat checks, 26 August 2026.

## Slide 5
KEY DATA & RESULTS · 2 OF 5
Independent checks confirm the Ra20 run is internally consistent
Current at peak power, repeatability, and generator scaling support the same interpretation
Source: Ra20 sweep summary, repeat checks, and generator-model audit, 26 August 2026.
Chart: Current at peak power vs wind speed
| 10.1 | 18.6 | 29.1 | 37.5
I at Pmax (A) | 0.018 | 0.068 | 0.24 | 0.32
Chart: Repeat-check difference (%)
| Check 1 | Check 2
Difference (%) | 0.3 | 0.2
Chart: Power-law exponent: measured vs model
| Measured | Predicted
Exponent | 3.77 | 3.79
The Ra20 electrical data are internally consistent; a surface-roughness effect has not yet been established across conditions.

## Slide 6
KEY DATA & RESULTS · 3 OF 5
Initial testing established a reference—but no significant blade separation
13-point load-variation record · 9.786–35.963 m/s · measured rotor rpm and maximum-power envelope
Sources: Summary_Table_Part1_MAX.csv and project email threads, 5 June and 27 July 2026.
Use this as the initial reference: Pmax reaches 3.01 W, and Jeong reported no significant blade differences. Condition metadata and uncertainty are incomplete.
Chart: Initial maximum-power envelope vs wind speed
| 9.8 | 12.0 | 14.0 | 16.2 | 18.4 | 20.6 | 22.8 | 25.0 | 27.2 | 29.4 | 31.6 | 33.8 | 36.0
Pdc,max (W) | 0.046 | 0.091 | 0.132 | 0.187 | 0.293 | 0.469 | 0.638 | 1.202 | 1.351 | 2.063 | 2.078 | 2.352 | 3.007
Chart: Initial measured rotor speed vs wind speed
| 9.8 | 12.0 | 14.0 | 16.2 | 18.4 | 20.6 | 22.8 | 25.0 | 27.2 | 29.4 | 31.6 | 33.8 | 36.0
Measured rotor rpm | 75.2 | 121.1 | 170.2 | 184 | 227.3 | 238.7 | 268.8 | 290.5 | 306.9 | 365.9 | 424 | 419.4 | 486.9

## Slide 7
KEY DATA & RESULTS · 4 OF 5
No-texture baseline reaches 5.60 W and 618 rpm before the final point
16-point no-texture run · 9.786–42.525 m/s · rotor rpm recorded
Source: Summary_Table.csv attached to “Updated Test Data – Wind turbine,” 27 July 2026.
Power reaches 5.60 W; rpm peaks at 618 then falls 3.7% at the final point. The baseline protocol differs from Ra20.
Chart: Peak DC power (W) vs wind speed
| 9.8 | 12.0 | 14.0 | 16.2 | 18.4 | 20.6 | 22.8 | 25.0 | 27.2 | 29.4 | 31.6 | 33.8 | 36.0 | 38.2 | 40.3 | 42.5
Pdc,max (W) | 0.33319 | 0.53319 | 0.50826 | 0.60749 | 0.76771 | 0.91839 | 1.0159 | 1.3404 | 1.8253 | 2.2531 | 2.6113 | 3.1026 | 3.8179 | 4.3041 | 5.0725 | 5.6016
Chart: Measured rotor speed (rpm) vs wind speed
| 9.8 | 12.0 | 14.0 | 16.2 | 18.4 | 20.6 | 22.8 | 25.0 | 27.2 | 29.4 | 31.6 | 33.8 | 36.0 | 38.2 | 40.3 | 42.5
Measured rotor rpm | 103.9294 | 132.7987 | 178.9896 | 167.4419 | 219.4066 | 236.7281 | 254.0497 | 271.3713 | 352.2053 | 375.3007 | 404.17 | 461.9086 | 508.0994 | 554.2903 | 617.8027 | 594.7073

## Slide 8
KEY DATA & RESULTS · 5 OF 5
Ra20 remains below the July no-texture baseline at matched wind speeds
Observed difference falls from 91.7% to 8.8% across four shared wind references; protocols differ
Sources: smooth Summary_Table.csv, 27 July 2026; Ra20 automated sweep summary, 26 August 2026.
The narrowing gap is descriptive, not causal: smooth values are interpolated and protocols, rotor-speed capture, and uncertainty differ.
Chart: Pmax (W) at four common wind-speed references
| 10.1 | 18.6 | 29.1 | 37.5
Smooth baseline — interpolated | 0.361 | 0.782 | 2.195 | 4.16
Ra20 — measured | 0.03 | 0.273 | 1.665 | 3.793
DESCRIPTIVE GAP
Wind (m/s) | Ra20 below smooth
10.1 | 91.7%
18.6 | 65.1%
29.1 | 24.1%
37.5 | 8.8%
Linear interpolation; no shared uncertainty

## Slide 9
INTERPRETATION & NEXT STEP
Three numeric records strengthen the audit—not a roughness ranking
Initial reference, July no-texture baseline, and Ra20 are quantified; Ra80 extraction and a matched campaign remain required
PROTOCOL
14 / 14 Ra20 setpoints
REPEATABILITY
0.3% and 0.2% check differences
RECORD COVERAGE
3 numeric records
Initial reference + smooth + Ra20 · Ra80 pending · Ra40 missing
SUPPORTED BY PRESENT DATA
Initial 13-point record recovered; Jeong reported no significant differences. July no-texture baseline includes rotor rpm and Pmax. Ra20 sweep is complete; repeat checks agree within 0.3%.
NOT SUPPORTED YET
A four-condition roughness ranking. Cp(λ) or Cq(λ) without synchronized rotor rpm. A causal roughness claim from unmatched protocols.
Next: repair/extract Ra80, document the initial-test blade configuration, and run matched smooth/Ra20/Ra40/Ra80 tests with synchronized rotor rpm.
Evidence boundary based on project records reviewed through 9 September 2026.

## Slide 10
RECOMMENDED NEXT CAMPAIGN
A matched roughness and fault campaign will make the comparison decision-ready
Smooth · Ra20 · Ra40 · Ra80 plus predefined fault blades, synchronized rotor rpm, balanced order, repeats, and normalized analysis
01
Measure rotor speed
Acquire rotor rpm on the common DAQ; verify the channel and pulses per revolution.
02
Define specimens and order
Create a manifest for smooth/Ra20/Ra40/Ra80 and fault cases; use a balanced mounting sequence.
03
Repeat and reconcile
Repeat check points; reconcile wind-speed files; document load-control mode and blade identity for every run.
04
Normalize performance
Calculate λ, Cp(λ), and Cq(λ); compare smooth, Ra20, Ra40, and Ra80 at matched λ.
Completion criteria
Synchronized data
Rotor rpm aligned with wind and load measurements.
Specimen manifest
Surface condition and fault geometry documented.
Clean data trail
Point and summary records reconciled.
Decision-ready curves
Cp(λ), Cq(λ), repeats, and uncertainty.
Traceability: preserve raw, point-level, summary, and specimen metadata for every run.
Decision rule: report a roughness effect only if separation persists at matched λ across repeats and exceeds combined uncertainty.
Proposed completion protocol based on the present measurement and data audit.

## Slide 11
APPENDIX A · DATA INVENTORY
Three numeric records are recovered; two roughness conditions remain incomplete
Initial reference, July no-texture baseline, and Ra20 are quantified; Ra80 extraction failed and Ra40 was not located
Evidence status based on connected project records reviewed through 9 September 2026.
Condition | Available record | Interpretation status
Smooth | 27 Jul 2026 · 16-point smooth run | Quantified; procedure differs from Ra20
Ra20 | Complete 14-point automated sweep | Analyzed and repeatable; rotor rpm absent
Ra40 | No run located | Missing condition
Ra80 | Point + summary CSVs located | Numeric extraction and QA pending
Archive status: initial + smooth + Ra20 numeric · Ra80 pending extraction · Ra40 missing.

## Slide 12
APPENDIX B · CALIBRATION LINK
Measured fan rpm connects tunnel calibration to electrical output
Four audited reference points connect measured drive speed, wind speed, and Pmax
Source: Ra20 sweep summary and audited reference points, 26 August 2026.
Chart: Calibrated wind speed vs fan rpm
| 496 | 894 | 1384 | 1779
Wind speed (m/s) | 10.1 | 18.6 | 29.1 | 37.5
Chart: Peak electrical power vs fan rpm
| 496 | 894 | 1384 | 1779
Pmax (W) | 0.03 | 0.273 | 1.665 | 3.793
Fan speed links the controlled input to measured wind and Pmax; rotor rpm is still required for aerodynamic performance.

## Slide 13
APPENDIX C · GENERATOR MODEL
Generator exponents reconstruct the measured Ra20 power law
Voc ∝ v¹·⁵⁰ and Rint ∝ v⁻⁰·⁷⁹ predict n = 3.79—within 0.02 of measured 3.77
Source: generator-model audit and Wind Tunnel Logs, 26 August 2026.
Chart: Generator-model exponent magnitudes
| Voc growth a | Rint decay ¦b¦
Power-law exponent | 1.5 | 0.79
Chart: Exponent reconstruction: n = 2a − b
| 2a | −b | Predicted n | Measured n
Exponent contribution | 3 | 0.79 | 3.79 | 3.77
The 0.02 agreement validates the electrical generator model—not a blade-roughness ranking without matched Cp(λ) curves.